## Slide 1: Optimisation Experimental Design v3

## Slide 2: Equipment
6 pECI component combinations
6 donors
3 substrates – glass, metal and plastic
2 time periods – after deposition and 24 hours

## Slide 3: Experiment Overview
Each donor will donate one natural mark to each substrate totalling 18 fingermarks (6 individual marks per substrate).
Those fingermarks will be taken to PERL and recorded using all pECI combinations on a copy stand.
The same fingermarks and substrates will then be taken to the apartments and placed vertically on a wall for handheld photography using all pECI combinations.

## Slide 4: Experiment Overview
We want to use the same fingermarks and substrates across the PERL and apartments photos.
This is to provide clear donor and substrate variability (Glass, Metal and plastic)
If I was to choose various substrates built within the apartments/CSI house then I would be choosing substrates that tests the versatility of the pECI and not its capability to enhance fingermarks on different substrate materials in uncontrolled conditions.

## Slide 5: PERL Photography Aims
Compare all component combinations in controlled lighting situations
In PERL I can control ambient lighting and can set the flash to be consistent across all components.
Any difference in enhancement will be caused by the components themselves and not lighting.

## Slide 6: Apartments Photography Aims
Compare all component combinations in uncontrolled lighting conditions while handheld.
Can not adjust ambient light and flash placement. While the flash will be roughly the same, it still will be inconsistent. This is what the pECI is also designed for so it will give a more realistic view of the final optimised box capability.
Will inform us of the impact (if any) handheld pECI photography has on enhancement and will dictate my next step. I suspect from previous experiments and from play testing that handheld photography is having a larger impact than we realise, though the new casing might be reducing this impact there is only one way to find out.
I can also use this data to better support the removal of components based on their practicality in-field (weight, cost etc).

## Slide 7: DATA
UC grading (going to be a lot)
PERL Comparison - for example, pECI Combination 1 PERL images will be compared to pECI combination 2 PERL images.
Apartment Comparison - for example, pECI Combination 1 apartment images will be compared to pECI combination 2 apartment images.
Copystand vs handheld – for example, pECI Combination 1 PERL images will be compared to pECI combination 1 apartment images. This comparison is to understand the total impact handheld photography has.

## Slide 8: Time Frame
Since I have 6 donors and 6 pECI combinations I am splitting the experiment in two parts
Week one I will do the entire experiment with 3 donors.
Week two I will do the entire experiment with the other 3 donors.
This will ensure I am not rushing to take all images within one time frame.