## Slide 1: Optimisation of Optical Components

## Slide 2: Aims
Determine the best optical pECI component combination
Demonstrate optical pECI component combinations don’t suffer from handheld use
Demonstrate effect misalignment of substrate and flash unit has on final images

## Slide 3: Background Information
Easiest way to determine the best component combination is on a copy stand where variables such as being perpendicular to the substrate and flash unit angle and distance can be controlled.
Once you are handheld those variables are no longer controlled and have a potential to effect the final image. I need to demonstrate if this is a problem and if it is a major or minor issue.
Fresnel lens is a good example, works great on a copystand, but too difficult to use handheld.
Therefore I must test each component combination on a copy stand in ideal conditions and then handheld to determine if other components may suffer greatly once taken handheld.

## Slide 4: pECI Combinations
Combination Number | Semi-transparent Mirror | Diffuser
1 | CD Case | Acrylic
2 | Acrylic Two-way | Acrylic
3 | Beamsplitter | Acrylic
4 | CD Case | MateLux Glass
5 | Acrylic Two-way | MateLux Glass
6 | Beamsplitter | MateLux Glass

## Slide 5: Donors, substrates and aging periods
6 donors – each donating one natural fingermark to 3 substrates
Substrates include
  Glass
  Metal
  Plastic
Aging Period – either after deposition plus 24 hours, or I only age them 24 hours and record them.

## Slide 6: Data Collection
Split into two sections
Round 1 – copystand images
Round 2 – handheld images

## Slide 7: Data Collection - Round 1
Set up camera and flash unit so the flash is at an optimum length and angle from each pECI combination and device is confirmed to be perpendicular to the substrate.
Record all 18 fingermarks with each component combo
This will demonstrate capability of optical components in ideal conditions and should show each components true effect on the final image.

## Slide 8: Data Collection- Round 2
Take each component combo handheld and re-record the same fingermarks deposited on the same substrates.
Now I cannot confirm if the device is perpendicular and the flash unit will be at variable distances and angles from the pECI box.
Record all 18 fingermarks with each component combo
Determines capability of component combinations in uncontrolled conditions

## Slide 9: Data Analysis – Round 1
pECI Combo | Compared to pECI Combo |  |  |  | 
1 | 2 | 3 | 4 | 5 | 6
2 | 3 | 4 | 5 | 6 | 
3 | 4 | 5 | 6 |  | 
4 | 5 | 6 |  |  | 
5 | 6 |  |  |  | 
Copystand images compared to copystand images using UC grade
270 split images – (doubled if examine age)
Determines which combo performs best in controlled conditions

## Slide 10: Data Analysis – Round 2
pECI Combo | Compared to pECI Combo |  |  |  | 
1 | 2 | 3 | 4 | 5 | 6
2 | 3 | 4 | 5 | 6 | 
3 | 4 | 5 | 6 |  | 
4 | 5 | 6 |  |  | 
5 | 6 |  |  |  | 
Handheld images compared to handheld images using UC grade
270 split images – (doubled if examine age)
Determines which combo performs best in uncontrolled conditions

## Slide 11: Data Analysis – Round 3
Copystand images compared to handheld images using UC grade
108 split images – (doubled if examine age)
Determines the effect uncontrolled conditions have on each combo if any

## Slide 12: Bonus experiment
Strap camera and pECI to copystand
Adjust angle of camera, angle of flash to show what actually happens when this items aren’t aligned correctly.